ECEn 774
Final
Jae Lee

1. PD controller
No parameters change / Possible 100% change in parameters / PD controller seems to be very robust in parameter changes. As shown above, parameter changes didn't make any noticeable difference on performance of the controller.

2. Backstepping
No parameters change / Possible 50% change in parameters / Backstepping can't handle the uncertain parameters very well. The higher uncertainty is, the more steady-state error generated.

3. Feedback linearizing controller
No parameters change / Possible 50% change in parameters / Feedback linearizing controller can't handle the uncertain parameters very well. The higher uncertainty is, the more steady-state error generated. It is behaving similar to backstepping.

4. Sliding mode
No parameters change / Possible 50% change in parameters / Sliding mode is quite robust in uncertainty because the controller is usually designed based on the maximum or minimum values that the uncertain parameters can possibly be. It did a lot better in dealing with not precisely known parameters than backstepping or feedback linearizing controller.

5. Baseline + adaptive controller
Only baseline controller / Baseline + adaptive / Possible 50% change in parameters / Adaptive controller is very robust to uncertainties in parameters. The baseline controller itself is quite robust, but the baseline+adaptive is even better.